## Slide 1: Interface between RTOS target and an Industrial System: Developing USB Digital I/O Module
Benjamin O’Brien
4/29/2013

## Slide 2: Motivation
GTA for Real Time Lab
Students need practical experience with Real Time software constructs
Current Fischertechnik systems are aging
  Broken and worn parts frustrate students
  Configurations are limited
Need to find alternatives

## Slide 3: Alternatives
Most alternatives are directed towards PLC training
Physical Process Emulators
  Edibon PLCE ($1600)
  TII Technical Education Systems PAS Modules ($600)
  Designed for standard 24V PLC’s not GPIO
Visual Process Emulators
  Bradley PSIM PLC Simulator
  Easy Visualized Equipment Emulation Program (EasyVeep)

## Slide 4: Alternatives Cont.
PSIM PLC Simulator
  No nice way to connect to an external interface
  Program so old it won’t run on Windows 7
EasyVeep
  Software is free but required EasyPort is expensive
  EasyPort is designed for PLC not GPIO logic levels
  Could we build our own EasyPort?

## Slide 5: Proposed Solution
Create an EasyPort alternative to allow existing Real Time targets to interact with EasyVeep

## Slide 6: Creating an EasyPort
Searched the manufacture’s website for technical information related to EasyPort protocol
  Dead Links
Buying an EasyPort in order to reverse protocol was too expensive
Disassemble and analyze EasyVeep binaries!

## Slide 7: Analyzing EasyVeep
Hex-Rays Interactive Disassembler (freeware)
Analyzed various components of the EasyVeep software distribution to find Serial Protocol
  EasyVeep.exe
    Main executable, no serial communications code
  EasyPort.ocx
    ActiveX Control responsible for all communication to EasyPort.
    Has format of a Windows COM Object

## Slide 8: Analyzing EasyPort.ocx
Looked through the Virtual Method Table
  The vtable holds human readable names and pointers to the associated messages
Found many usefully named functions
  Connect, SetOutput, GetInputWord
Traced execution of each method of interest and found the format strings being used to build and decode commands

## Slide 9: EasyPort Protocol
Command Format | Description
setup0 | Request made by PC to initialize connected EasyPorts.
setup[1-4] | EasyPort response to setup0 command requesting a module number 1-4.
DV | Request by PC to get EasyPort version
V=\d.\d{2} | Response to version request containing the version number of the EasyPort. Must exceed (1.20).
MAW=[1-4].[0248]=[0-F]{4} | Modify the 16 bit output value of EasyPort module [1-4], channel log2([0248]) to be the value represented by hex number [0-F]{4}.
DEW[1-4].[0248] | Request the current input values from module [1-4], channel log2([0248])
EW[1-4].[0248]=[0-F]{4} | Response to input value request. The current value of the inputs is represented by a four digit hex number. DAW command is sent in response requesting the current out values the EasyPort has. A response to DAW is not required.
DAW[1-4].[0248] | Request the current output values from module [1-4], channel log2([0248]) . A response is not required in this application.

## Slide 10: EasyPort Protocol (2)

## Slide 11: Making an EasyPort Mark I
Arduino Uno R3
  Never meant to be final implementation, but useful as a proof of concept prototype
Fail-duino
  Arduino only ever received 0xFF serial characters
  AGG Software Advanced Serial Port Monitor
    Arduino can’t do the required flow control without modification!

## Slide 12: Making an EasyPort Mark II
Write a proof on concept emulator
Desktop application using com0com loopback
  com0com allows serial port emulation
Implemented discovered protocol
  Able to interact with EasyVeep simulations!

## Slide 13: Making an EasyPort Mark II (2)

## Slide 14: Making MyEasyPort
Stellaris Launchpad
  Overpowered, but available
  Supports the flow control EasyVeep desires
Implemented the protocol
  Everything talked well at low speed
  Updating at more the 5Hz crashed EasyVeep!
  Tried debugging EasyVeep and MyEasyPort
    Too hard to debug without EasyVeep source

## Slide 15: MyEasyVeep
EasyVeep simulations are just flash movies
  Copied the flash movies into my own project
Using Flash ActiveX control to load and play
How do I interact with the movie?
  Decompile the swf
    Sothink Flash Decompiler (trial)
    flasm –d
  Look through the disassembly to find variable names

## Slide 16: MyEasyVeep (2)
Sort through all the variable names to find the useful ones.
Use ActiveX GetVariable and SetVariable methods
Variable Name | Purpose
EprgName | English Program Name
EprgLeirasX | English Program Description ( X = 0..10)
EDigSensX | English Sensor Description ( X = 1..16)
EDigActX | English Actuator Description (X = 1..16)
DAX Digital | Actuator Value ( X =1..16)
DSX Digital | Sensor Value (X=1..16)

## Slide 17: MyEasyVeep (3)
Queried simulation at twice the frame rate
If sensor values changed, command would be sent to connected EasyPort
On Update command from MyEasyPort actuator variables would be set in swf
User can also interact with buttons on GUI
Auto – mode shows user how system should work when controlled correctly

## Slide 18: MyEasyVeep (4)

## Slide 19: MyEasyPort Design
Connecting MyEasyPort to Arcom is tricky
  Logic Levels are different
    3.3V MyEasyPort, 5V Arcom
  Line Buffers
    Arcom I/O card is very low current
  Proper Isolation is nice to have
    Ground loop, transient voltages
  32 channels of I/O need to be routed
    4 8-bit channels
    Pin-out on Arcom is bizarre

## Slide 20: MyEasyPort Design (2)
Silicon Labs Si84XX CMOS isolator
  Level shifting, line buffering, isolating package
    Everything in one inexpensive IC
    It’s only available in SMD packages
  4 channels of I/O at up to 150Mbs (using ~15bps)
  Chose Si8442
    2 Channels each way
    Low power consumption so Arcom and USB can power it

## Slide 21: MyEasyPort Design (3)
Used Excel to Experiment with Pin Outs

## Slide 22: MyEasyPort Design (4)

## Slide 23: Using in a VxWorks Program
User must control the I/O mode of the Digital I/O Card
Switching between modes takes some time
  about 500 micro seconds
  This can lead to an occasional timing glitch
void setActuatorValues(int Actuators){
sysOutByte(0x184,0x01); /* Re enable outputs */
sysOutByte(0x183,(Actuators & 0xFF00) >> 8);
sysOutByte(0x181,(Actuators & 0x00FF));
}
int getSensorValues()
{
int iSensors = 0;
sysOutByte(0x184,0x00); /* Disable outputs */
iSensors = (sysInByte(0x182) << 8) | (sysInByte(0x180));
sysOutByte(0x184,0x01); /* Re enable outputs */
return iSensors;
}

## Slide 24: Conclusions and Recommendations
MyEasyPort and MyEasyVeep provide an easy to use interface to many valuable simulations
Students will have access to more systems with which they can interact
Software simulations will not break and fail in the same manner as current systems used
Additional system simulations can be created easily with Adobe Flash or any project the can produce Flash movies

## Slide 25: Conclusions and Recommendations (2)
In the future
  Create additional simulations
  Make a smaller, cleaner MyEasyPort
  Resolve the small glitch from switching the I/O card from Input to Output mode
  Add features to MyEasyVeep to assists student learning and comprehension further

## Slide 26: Demonstration
Demonstration of the MyEasyPort and MyEasyVeep software will take place in LB161.

## Slide 27: References
[1] | L.-X. Li, H. M. Lu, L. ZhiPing and M. XiangYang, "Design and Application of Automatic Control System Program Based on FESTO Training System," in Control, Automation and Systems Engineering (CASE), 2011 International Conference o, 2011.
[2] | A. R. Izaguirre and M. E. Macias, "Virtual Reality Machines to improve training in Control and Automation," in Conference for Industry and Education Collaboration, San Antonio, 2011.
[3] | D. Wolowicz and J. Knoll, "Proposal For USB I/O Board," 13 May 2002. [Online]. Available: http://www.ece.uvic.ca/~elec499/2002a/group04/Proposal.pdf. [Accessed 10 12 2012].
[4] | L. Ngalamou and L. Myers, "A Software Approach for the Design of a Virtual Plant," International Journal of Computer Science and Network Security, vol. 10, no. 9, pp. 48-56, 2010.
[5] | C.-G. Haba, "Extending the Use of PLC Simulator Software in Student Laboratory Works," Advances in Electrical and Computer Engineering, vol. 10, no. 1, pp. 84-89, 2010.
[6] | Sealevel, "The Digital I/O Handbook ¦ Sealevel Support," 08 05 2012. [Online]. Available: http://www.sealevel.com/support/article/AA-00391/155/Resource-Center/Digital-IO-Interfaces/The-Digital-IO-Handbook.html#CL. [Accessed 19 12 2012].
[7] | "PSIM PLC Training Simulator," The Learning Pit, [Online]. Available: http://www.thelearningpit.com/plc/psim/psim.html. [Accessed 23 January 2013].
[8] | Festo Didactic GmbH & Co., "Manual EasyPort USB," 1 11 2008. [Online]. Available: http://www.festo-didactic.com/ov3/media/customers/1100/721876_deenesfr_mit_lesezeichen_4.pdf. [Accessed 19 11 2012].
[9] | Hex-Rays, "Freeware Download Page," [Online]. Available: http://www.hex-rays.com/products/ida/support/download_freeware.shtml. [Accessed 11 29 2012].
[10] | "Null-modem emulator," [Online]. Available: http://com0com.sourceforge.net/. [Accessed 12 Dec 2012].
[11] | Silicon Labs, "HIGH-SPEED LEVEL SHIFTING USING Si8XXX ISOLATORS," [Online]. Available: http://www.silabs.com/Support%20Documents/TechnicalDocs/AN598.pdf. [Accessed 5 March 2013].
[12] | Sealevel, "USB to 16 Isolated Inputs / 16 Reed Relay Outputs Digital Interface Adapter (8221)," [Online]. Available: http://www.sealevel.com/store/i-o/digital-i-o/usb/8221-usb-to-16-isolated-inputs-16-reed-relay-outputs-digital-interface-adapter.html. [Accessed 19 12 2012].
[13] | Festo Didactic GmbH & Co., "ActiveX Control for EasyPort USB," [Online]. Available: http://www.festo-didactic.com/int-en/services/software/software-licences/activex-control-for-easyport-usb.htm?fbid=aW50LmVuLjU1Ny4xNy4zMi44MjUuNjk0NQ. [Accessed 28 11 2012].

## Slide 28: Questions?